General Rules:
A command will be executed upon the reception of <LF>.
Any wrong command will return „E“.
A return value ends with <CR> <LF>.
A list of return values is separated by <CR> <LF>.

Exit
Terminate session. Keep state of master.

SetTimeout(timeoutSec)
Enables or disables Connection State supervision. Will terminate connection after {timeoutSec} sec without traffic.

Parameters:
timeoutSec	n	timeout in seconds (default = 30, 0 = disabled)

Return:
timeout=	n	in seconds

KeepAlive
prevents Connection Timeout

Return:
	1

ListDevices
Returns List of found USB FTDI devices

Return:
	n	Number of devices, list with devices follows
	dev0	Only if devices are found
	...

OpenSerial(serial)
Open connection to selected FTDI Master by device serial number.

Parameters:
serial number	n	serial number of device

Return:
connected=	[0|1]

Close
Close connection to FTDI Master. Stop Periodic Transfers.

Return:
connected=	[0|1]

SetBitrate(bitrate)
Select Bitrate

Parameters:
bitrate	n	in baud (default = 500000)

Return:
bitrate=	n

SetSync(sync)
Select SYNC

Parameters:
sync	8 (default)	bit
	32	bit

Return:
sync=	n

SetHeader(header)
Select Header format

Parameters:
header	3 (default)	byte header
	4	byte header

Return:
header=	n

SetParity(parity)
Select Parity

Parameters:
parity	0 (default)	Even
	1	Odd
	2	Space
	3	None

Return:
parity=	n

SetBreak(break)
Select Break Length

Parameters:
break	x,y	double format (default = 13,5)

Return:
break=	x,y

SetNodeAddr(addr)
Select address of node.

Parameters:
addr	n

Return:
addr=	n

SendWakeup(symbol, ack)
Send Wakeup, symbol if selected, ack if selected.

Parameters:
symbol	[0|1]	1: send wakeup symbol + sleep 25ms
ack	[0|1]	1: send wakeup ack

Return:
	1

SendSleepBroadcast
Send Broadcast for Sleep.

Return:
	1

Write(addr, words, data)
Write {words} data words starting with {addr} with the same {data}. Address will be auto-incremented by 2.

Parameters:
addr		Byte address in decimal or hex
words		number of words in decimal
data		write data in decimal or hex

Return:
	[0|1]

Read(addr, words)
Read {words} data words starting with {addr}. Address will be auto-incremented by 2.

Parameters:
addr		Byte address in decimal or hex
words		number of words in decimal

Return:
	[0|1]	1: list with read data follows
	data0
	…

Verify(addr, words, mask, expected)
Verify {words} data words starting with {addr}, checking that {expected} =? (rdata & {mask}). Address will be auto-incremented by 2.

Parameters:
addr		Byte address in decimal or hex
words		number of words in decimal
mask		verify mask in decimal or hex
expected		expected check value in decimal or hex

Return:
	[0|1]	0: list with read data follows
	data0
	…

SetPeriodicWrite(addr, data, words)
Enable periodic write of {words} data words starting with {addr} with the same {data}. Address will be auto-incremented by 2.

Parameters:
addr		Byte address in decimal or hex
words		number of words in decimal (0 = disable)
data		write data in decimal or hex

Return:
	1

SetPeriodicVerify(addr, words, mask, expected)
Enable periodic verify of {words} data words starting with {addr}, checking that {expected} =? (rdata & {mask}). Address will be auto-incremented by 2.

Parameters:
addr		Byte address in decimal or hex
words		number of words in decimal (0 = disable)
mask		verify mask in decimal or hex
expected		expected check value in decimal or hex

Return:
	1

SetPeriodicIntervalMs(interval)
Set interval in ms between periodic transfers.

Parameters:
interval	n	in ms

Return:
interval=	n

StartPeriodic
Start/Enable configured periodic transfers.

Return:
periodic=	[0|1]

StopPeriodic
Stop/Disable periodic transfers.

Return:
periodic=	[0|1]

GetStatus
Returns and clears status flags

Return:
com_error=	[0|1]	Any error detected during transfer (readback, response, timeout, …)
verify_error=	[0|1]	Verify error has occurred.

GetLastLiveCounter
Returns last used Live Counter

Return:
	n

SetDebugHeaderCrcError(debugHeaderCrcError)
Select injection of Header CRC Error

Parameters:
debugHeaderCrcError	[0|1]

Return:
debugHeaderCrcError=	[0|1]

SetDebugWriteCrcError(debugWriteCrcError)
Select injection of Write CRC Error

Parameters:
debugWriteCrcError	[0|1]

Return:
debugWriteCrcError=	[0|1]

SetDebugUseLastLiveCounter(debugUseLastLiveCounter)
Select injection of LiveCounter Error

Parameters:
debugUseLastLiveCounter	[0|1]

Return:
debugUseLastLiveCounter=	[0|1]